Data Item Description

Level 2 Design Guidance Data

DID E003

Prepared by:	Vancouver Shipyards Co. Ltd.

2 Pemberton Ave.

North Vancouver, BC, Canada, V7P 2R2

Tel:  (604) 988-3111

Fax: (604) 984-1636

© Vancouver Shipyards Co. Ltd. 2016

# Purpose

Level 2 Design Guidance Data is required to enable the final design of the Ship to proceed.

# Scope

Information as required below .

# References

This DID must be read in conjunction with Part 3 (Engineering) of Schedule D1 (SOW).

# Preparation Instructions

The supplier shall provide a DID Compliance Matrix indicating which submission files contain the items listed in this DID.

For written style documents (eg. manuals, performance specification documents, etc) larger than 10 pages the document shall include a Table of Contents that contains links to the various section headers within the document.

## Content and Format

All physical parameters quoted at this stage are to be the actual final design standard.

Level 2 Design Guidance Data includes, where applicable:

- Update to all information and Equipment Specification Table entries provided in SDRLs E001 and E002 and DIDs E001 and E002. Note, if a piece of information is not updated in this submittal it is by default implied to be “the actual final design standard” per the statement above.

- All Connection Data, to enable connectors to be made up, without additional information (e.g. from third party connector manufacturers).  As a minimum this data must include:

- preparation of cable cores, screens and insulation

- screen termination definition and procedures

- core termination procedures

- heat-shrink boot fitting procedures

- A comprehensive list of cable and connection tools necessary for correct installation of mating connectors and backshells or heat shrink glands and boots.  The list is to include all necessary crimping, insertion and extraction tools, and must highlight tools peculiar to one particular cable/connector type or manufacturer.

- Any specialised technical information not already included in SDRL’s E001 and E002.

## Structure

Separate file submission where appropriate (eg. Where the information requested does not reside as part of an interconnectivity diagram or the Equipment Specifications Table).

# Special Instructions

#### Supplier must provide an update to information provided with SDRLs E001 and E002 and DIDs E001 and E002 where applicable. Changes to the information provided must be clearly identified.

Information that pertains to physical dimensions and arrangements shall be provided in AutoCAD format (.dwg).