Data Item Description

EMC Qualification Test Report

DID E302

Prepared by:	Vancouver Shipyards Co. Ltd.

2 Pemberton Ave.

North Vancouver, BC, Canada, V7P 2R2

Tel:  (604) 988-3111

Fax: (604) 984-1636

© Vancouver Shipyards Co. Ltd. 2016

# Purpose

The Electromagnetic Compatibility Qualification Test Report (EMCQTR) is a description and report of the EMC testing performed on the Subcontractor’s Equipment.

# Scope

The EMC Qualification Test Reports are used to describe and record the results of one or more EMC tests defined in the Test & Acceptance Plan.  The EMC Qualification Test Reports summarise test discrepancies and references the corresponding problem/change reports.

# References

This DID must be read in conjunction with the SOW.

# Preparation Instructions

## Content

Media

The document shall be supplied both in hard and soft copies. The hard copies shall take the form of an A4 size document, bound in ring binders.

Detailed Content

This document shall consist of the following:

- Front Matter

- Scope

- Referenced documents

- Test Report

- Details of the tests conducted and standards achieved

### Front Matter

This section shall include a title page, list of contents, change and issue status and any other material required by the Subcontractor’s documentation procedures.

### Scope

This section shall include but not be limited to the following items:

- Identification.

The approved identification number, Title, and abbreviation, if applicable, of the system to which 	his EMCQT Report applies

- System overview.

The Purpose of the system to which this EMCQT Report applies.

- Document overview.

This paragraph shall summarise the Purpose and contents of this document.

- Relationship to other plans.

The relationship, if any, of this Report to the Subcontractor Trials & Acceptance Plan and associated EMCQT Schedule or Report.

#### Applicable Documents.

A list by document number and Title of all documents referenced in this EMCQT Schedule.

#### Test Report

This section shall be divided into paragraphs and subparagraphs as appropriate to describe the environmental qualification test of the deliverable item, detailing each separately identified test. The order of tests within this document shall correspond to the order of tests within the EMCQTS. The information provided shall include but not be limited to the following for each test carried out during the EMCQT:

- Identifier of the test, including test name.

- Summary of test results, including success/failure and problems identified.

- Chronological record of events relevant to test preparation, performance & analysis.

- Detailed test results.

- Deviations from the test procedure.

- Evaluation of impact on the Equipment of deficiencies identified.

- Proposed programme to rectify design shortcomings identified.

#### Notes.

This section shall contain any general information that aids in understanding this document (e.g., background information, glossary).  This section shall include an alphabetical listing of all acronyms, abbreviations, and their meanings as used in this document.

#### Appendices.

Appendices may be used to provide information published separately for convenience in document maintenance (e.g. charts, classified data).  Where available this section shall include any Graphs, response curves etc. supplied by the Test House during the course of testing.  As applicable, each appendix shall be Referenced in the main body of the document where the data would normally have been provided.

## Structure

Nil.

# Special Instructions

Nil